## Slide 1
Antenna Summit
<number>

## Slide 2
Session 3 – Components
Chapter 4.1 to 4.5.6
+ Other Material

## Slide 3
Instructor:
Phil Brunner – AE7OH (was K9DTD, W6GOL)
ARRL HANDBOOK for Radio Communications
– (Reference for detailed information)
Q & A via Chat or at the end of each hour
Email questions to: phil.brunner@gmail.com
Viewgraphs are at http://HamRadioEdu.com

## Slide 4
Chapter 4 – Components
The World of electronics is changing rapidly
    Landlines replaced by Cell Phone, Zoom, Skype
    Vacuum Tubes Disappearing – (Light Bulbs, CRTs, Radio Tubes)
Computers and DSPs are replacing individual components and units.
Software Defined Radios are available today.
We will concentrate on characteristics and skip the details!

## Slide 5
Components Characteristics
Practical Resistors, Capacitors and Inductors
Transformers
Semiconductors
Amplifiers
Vacuum Tubes
Circuit Simulation and AnalysisTools
Antennas and Tuners
Software Defined Radios and Units

## Slide 6
Starting Big - 112-foot
112-foot Goldstone
Deep Space
Antenna
with Subreflector

## Slide 7
Satellite Antennas Defense Support Program Chandra Xray Telescope https://en.wikipedia.org/wiki/Defense_Support_Program https://en.wikipedia.org/wiki/Chandra_X-ray_Observatory

## Slide 8
Resistors
Wire size suitable for max current
Resistance usually increases with temperature
Component Resistors
      Carbon, Metal-oxide
      Wirewound- low-frequency due to inductance
      Metal-film, Carbon-film – deposit on insulating substrate
Power rating and temperature stability are considerations
Tolerance often unimportant – 20%, 10%, 5%, 1%
Potentiometers – variable resistors

## Slide 9
Resistors

## Slide 10
Capacitors
Ideally blocks DC, no leakage, no energy loss
Tolerance and temperature coefficient
Voltage rating and breakdown
Frequency, resistance, leakage, inductance considerations
Ceramic, plastic film, mica, electrolytic, air-variable, vacuum
Electrolytics are high capacity and polarized - low frequency filtering

## Slide 11
Capacitors

## Slide 12
Inductors
Air-core or iron-core
Encapsulated (looks like resistor)
Slug tuned (variable)
  magnetic or non-magnetic core inside coiled inductor
  Adjust with screw-driver

## Slide 13
Inductors

## Slide 14
Transformers

## Slide 15
Switching Power Supply (Conceptual)
- Use high frequency to minimize transformer size/weight
- Needs careful design/shielding to avoid HF interference

## Slide 16
Semiconductors
Diodes – Point Contact, Pin, Schottky, Varactor, Zener
  Current, PIV, Speed, Reverse Current
Transistors – BJT, JFET, MOSFET
  Gain, Operating Regions and Parameters
Optical – Photo, LED, Laser, Optoisolators
Fiber Optics

## Slide 17
Some Semiconductor Symbols

## Slide 18
NPN Amplifier

## Slide 19
811A Vacuum Tube Push-Pull Final

## Slide 20
TOOLS
Arduino UNO + Breadboard
QUES – Quite Universal Circuit Simulator (Free)
  https://sourceforge.net/projects/qucs/files/latest/download
Circuit Calculations with Complex Numbers and Spreadsheets (Excel or LibreOffice CALC)
  Free LibreOffice Download: https://www.libreoffice.org/
Software Modems
Software Defined Radios

## Slide 21
Arduino and Breadboard CQ CQ DE AE7OH K

## Slide 22
Arduino+Breadboard Schematic
Arduino

## Slide 23
QuiteUniversalCircuitSimulator https://sourceforge.net/projects/qucs/files/latest/download
Manual: http://qucs.sourceforge.net/docs/tutorial/getstarted.pdf

## Slide 24
RLC
Transient
Simulation

## Slide 25
RLC
Frequency
And
Transient
Simulations

## Slide 26
Simple Power Supply

## Slide 27
Regulated Power Supply

## Slide 29
Pictures
MODEM IS ENTIRELY SOFTWARE

## Slide 32
Alternating Current Sinusoids
Radius rotates at f cycles per second to create sinusoid
imaginary
real

## Slide 33
AC Representation Choice for Calculations
Eli the Ice man
Complex Numbers
(easy calcs)
Polar form
Vectors

## Slide 34
Calculate Tuned Antenna Impedance

## Slide 35
Tuner Calc Spreadsheet (See Figure 24.4 in Antenna Book)

## Slide 36
Excel or CALC Complex Functions

## Slide 37
Tuner Adjustments
Tuner adjusted 5-Ohm Antenna to 38 ohms
Ant. Book assumed Q-values for components
Added Q-Resistors yield 50 ohms

## Slide 38
Tuner Reactance Tweaks
Minor phase error in answer can be removed by changing C1 to zero the reactance error
C2 can be adjusted to compensate for a reactive component in the Antenna:
    Decrease C2 to compensate for inductive antenna
    Increase C2 to compensate for capacitive antenna
Antenna design would probably try to make antenna nearer to the ideal 50-ohm, 0-reactance impedance at the desired frequency(s)
Stay tuned!

## Slide 39
Match1

## Slide 40
Match2
Input voltage: 100V
But peak voltages across tuner elements are 1000V

## Slide 41
High RF Tuner Voltages
High Voltage in tuner elements
  100 volts peak source
  1000 volts peak across components
Arcing and RF burns potential
Solutions include better antenna design
  e.g., a Balun can help match
Example: 5:1 transformer
Matches 50 ohm coax
To 300 ohm antenna
50
300

## Slide 42
Internet Antenna
CHA TD LITE HF Antenna

## Slide 44
RTL-SDR Software Defined Radio

## Slide 45
GQRX
(Linux)
or
SDR-Sharp
FM
Radio
Station

## Slide 46
SDR
VHF
Station

## Slide 47
Handhelds

## Slide 48
20 Meter Antenna