## Slide 1
Antenna Summit
<number>

## Slide 2
Session 3 – Components
Chapter 4.1 to 4.5.6
+ Other Material

## Slide 3
Instructor:
Phil Brunner – AE7OH (was K9DTD, W6GOL)
ARRL HANDBOOK for Radio Communications
      – (Reference for detailed information)
Q & A via Chat or at the end of each hour
Email questions to: phil.brunner@gmail.com
Viewgraphs are at HamRadioEdu.com

## Slide 4
Chapter 4 – Components
The World of electronics is changing rapidly
    Landlines replaced by Cell Phone, Zoom, Skype
    Vacuum Tubes Disappearing – (Light Bulbs, CRTs, Radio Tubes)
Computers and DSPs are replacing individual components and units (e.g., Modems)
We will concentrate on characteristics and skip the details!

## Slide 5
Components Characteristics
Practical Resistors, Capacitors and Inductors
Transformers
Semiconductors
Circuit Simulation and AnalysisTools
Examples

## Slide 6
Resistors
Wire size suitable for max current
Resistance usually increases with temperature
Component Resistors
      Carbon, Metal-oxide
      Wirewound- low-frequency due to inductance
      Metal-film, Carbon-film – deposit on insulating substrate
Power rating and temperature stability are considerations
Tolerance often unimportant – 20%, 10%, 5%, 1%
Potentiometers – variable resistors

## Slide 7
Resistors

## Slide 8
Capacitors
Ideally blocks DC, no leakage, no energy loss
Tolerance and temperature coefficient
Voltage rating and breakdown
Frequency, resistance, leakage, inductance considerations
Ceramic, plastic film, mica, electrolytic, air-variable, vacuum
Electrolytics are high capacity and polarized - low frequency filtering

## Slide 9
Capacitors

## Slide 10
Inductors
Air-core or iron-core
Encapsulated (looks like resistor)
Slug tuned (variable)
  magnetic or non-magnetic core inside coiled inductor
  Adjust with screw-driver

## Slide 11
Inductors

## Slide 12
Transformers

## Slide 13
Switching Power Supply (Conceptual)
- Use high frequency to minimize transformer size/weight
- Needs careful design/shielding to avoid HF interference

## Slide 14
Semiconductors
Diodes – Point Contact, Pin, Schottky, Varactor, Zener
  Current, PIV, Speed, Reverse Current
Transistors – BJT, JFET, MOSFET
  Gain, Operating Regions and Parameters
Optical – Photo, LED, Laser, Optoisolators

## Slide 15
TOOLS
Arduino UNO + Breadboard
QUES – Quite Universal Circuit Simulator (Free)
      https://sourceforge.net/projects/qucs/files/latest/download
Circuit Calculations with Complex Numbers and Spreadsheets (Excel or LibreOffice CALC)
      Free LibreOffice Download: https://www.libreoffice.org/

## Slide 16
Arduino and Breadboard CQ CQ DE AE7OH K

## Slide 17
Arduino+Breadboard Schematic
Arduino

## Slide 18
QuiteUniversalCircuitSimulator https://sourceforge.net/projects/qucs/files/latest/download
Manual: http://qucs.sourceforge.net/docs/tutorial/getstarted.pdf

## Slide 19
Some Semiconductor Symbols

## Slide 20
RLC
Transient
Simulation

## Slide 21
RLC
Frequency
And
Transient
Simulations

## Slide 22
Simple Power Supply

## Slide 23
Regulated Power Supply

## Slide 26
Alternating Current Sine Waves
Radial rotates at f cycles per second to create a sine wave
Imaginary axis
( j or i )
Real axis

## Slide 28
AC Representations
Vectors
Polar Form
Complex Numbers
(easy calculations)

## Slide 29
Calculate Impedance Match

## Slide 30
Impedance Match Calc Spreadsheet (See Figure 24.4 in Antenna Book)

## Slide 31
Excel or CALC Complex Functions

## Slide 32
Adjustments for Component Q
Match adjusted 5-Ohm Antenna to 38 ohms
Ant. Book assumed Q-values for components
Added Q-Resistors yield 50 ohms

## Slide 33
Match
Input voltage: 100V
But peak voltages across tuner elements are 1000V

## Slide 34
High RF Tuner Voltages
High Voltage in tuner elements
  100 volts peak source
  1000 volts peak across components
Arcing and RF burns potential
Solutions include better antenna design
  e.g., a Balun can help match
Example: 5:1 transformer
Matches 50 ohm coax
To 300 ohm antenna
50
300

## Slide 35
<number>
Questions?
You may email questions later to
phil.brunner@gmail.com

## Slide 36
SDR -
Software
Defined
Radio
GQRX (Linux, etc.) https://gqrx.dk/download
SDR# (Windows) https://airspy.com/download/